## Slide 1: SWBAT identify the major air pollutants and where they come from.
APES Unit 9 2/24/16

## Slide 2: Unit 9: Air
Ch. 15: Air Pollution and Stratospheric Ozone Pollution
1 week
Vehicle Exhaust emissions lab
EQs:
  How does air quality affect our lives?
  What are humans doing to change the air quality for better or for worse?
  Current Event Presentation: Attia on Mar. 4th

## Slide 3: Agenda
Lecture
Article
Videos

## Slide 4: Air Pollution
Pollution is in the troposphere (ground-level pollution)
Pollution in the atmosphere that can harm:
  Animals
  Buildings
  Alter ecosystems
Air pollution is global!
  Ex: South Asian Brown Cloud

## Slide 5: Primary vs. Secondary Air Pollutants
Primary air pollutants: released directly into the atmosphere and are toxic
  Ex: CO, SO2, NOx, many VOCs
Secondary air pollutants: formed by the combination of primary pollutants in the atmosphere.
  Ex: Ozone, SO42- and NO3-

## Slide 6: The Major Culprits (Criteria Pollutants) Remember: NOS CLP
Nitrogen Dioxide (NO2)
Ozone (O3)
Sulfur Dioxide (SO2)
Carbon Monoxide (CO)
Lead (Pb)
Particulates

## Slide 8: SO2 (sulfur dioxide)
Colorless gas with a strong odor
Respiratory irritant and can damage plant tissue
Primary source: combustion of fossil fuels (coal and oil)
Other sources:
  Metal smelting, paper pulping, volcanic eruptions, forest fires

## Slide 9: Nitrogen Oxides (NOx)
Nitrogen and oxygen react as a result of exposure to high temperatures:
  NO
    Colorless, odorless gas
    N2 + O2 2NO
  NO2
    Pungent, reddish brown gas
    2NO + O2 2NO2
Health effects: respiratory irritant, increases susceptibility to respiratory infection
Produced by combustion engines burning fossil fuels
Natural sources: forest fires, lightning, microbial action in soils

## Slide 10: Carbon Oxides (CO and CO2)
Carbon Monoxide (CO)
  Odorless, colorless gas
  Main sources: byproduct of incompletely burned organic material, such as fossil fuels
    Can be indoor air pollutant when exhaust systems on natural gas systems malfunction
  Effect on human health:
    Binds to hemoglobin and displaces oxygen
    In high concentrations, CO can be deadly

## Slide 11: Particulate Matter (PM)

## Slide 12: Particulate Matter (PM)
Small solid or liquid particles suspended in the air
Sources: combustion of wood, animal manure, biofuels and fossil fuels, volcanoes, unpaved roads
  Mainly diesel fuel engines
Health effects: exacerbate respiratory and cardiovascular diseases and reduce lung function
  Ex: soot and sulfate aerosols
Particulate matter less than 2.5 um is most dangerous to human health
  Composed of more toxic substances
  Deposited more deeply within the respiratory tract
Haze: particulate matter from air pollution scatters light

## Slide 13: Photochemical Oxidants
Oxides: oxidize (remove electrons) from other substances
Formed as a result of sunlight acting on compounds such as nitrogen oxides and sulfur dioxide
NOx, O3 and PANs
Tropospheric Ozone (O3) is most abundant and photochemical oxidant
  VOC + NOx + O2 + sunlight O3 + photochemical oxidants
  Harmful to plants and animals
  Can cause emphysema (damages air sacs in lungs, causes you to be out of breath)

## Slide 14: Photochemical Oxidants

## Slide 15: Smog
Smoke + fog = smog
Industrial smog (gray smog or London-type smog)
  Result of burning oil or coal
    CO and CO2 are released and combine with particulate matter to produce smog
  SO2 + H2O  H2SO4
  Tiny particles such as salt and the carbon in soot give smog its gray color
  Accounts for 750,000 deaths each year in China

## Slide 16: Photochemical Smog (Brown Smog)
Dominated by oxidants (O3)
Common cities with high brown smog: L.A. and Athens
  Commuter traffic!
Secondary pollutants that are a component of photochemical smog: O3, PANs, NO2, HNO3, H2SO4

## Slide 17: Photochemical Smog

## Slide 18: Lead (Pb) and other Metals
Lead present in small quantities in fossil fuels
  Added to gas to improve vehicle performance
    Phased out in U.S.
  Human health effects: nervous system disorders
Mercury (Hg)
  Released into atmosphere from burning of coal
  Human health effects: nervous system disorders

## Slide 19: Volatile Organic Compounds (VOCs)
Organic compounds that become vapors at typical atmospheric temperatures
  Hydrocarbons, terpenes and methane
  Source: Natural gas wells, cow belches, landfills, cleaning compounds, dry cleaning
  Play important role in the formation of ozone

## Slide 20: Let’s review!
What are the major air pollutants?
What is the difference between a primary and a secondary air pollutant?
Describe the difference between industrial smog and photochemical smog

## Slide 21: Homework
Read in textbook through page 419
Study Figure 15.7 in the textbook for formation of tropospheric ozone and photochemical smog
Make a flash card for one of the secondary pollutants involved in photochemical smog and list (look at table 15.1):
  How it is formed
  One effect on human health
  One environmental effect