## Slide 1: SWBAT explain the implications of landfills and incineration.
APES Unit 10 3/8/16

## Slide 2: Announcements
Ch. 16 Quiz on Thurs!!

## Slide 3: PAYT programs
Pay-As-You-Throw: charge municipal customers for the amount of household garbage they throw away
Incentive programs: bottle redemption bill
  Ex: Michigan: every bottle can be redeemed for 10 cents

## Slide 5: Compost
Organic materials: food and yard waste
In landfill: Anaerobic conditions organic matter decomposes and produces methane
Compost: organic matter that has decomposed under controlled conditions to produce organic-rich material that enhances soil structure, cation exchange capacity, and fertility

## Slide 6: Compost
Compostable items:
  Vegetable scraps
  Eggshells
  Coffee grounds
  Sawdust
  Yard clippings
  NO meat, fish, cheese etc.

## Slide 7: Compost
Important components:
  Ratio of 30:1 for Carbon: Nitrogen is best for microbial activity
  Frequent turning
  Appropriate moisture levels
  Respiration activity of microbes generates enough heat to kill pathogenic bacteria
Advantages:
  enhances soil quality
  Diverts waste from landfills
  Reduces methane emissions
Disadvantages:
  Takes time and space
  Sorting organic material prior to composting can attract flies or vermin

## Slide 8: Disposal of Solid Waste
Open Dumps: attracts pests and pollutes the air
Harmful components of MSW:
  Runoff
  Leachate: Water that leaches through the solid waste and removes various chemical compounds
  Solution for preventing groundwater contamination by leachate:
    Applying clean water continuously
    collecting the resulting flow of leachate
    processing this leachate

## Slide 9: Disposal of Solid Waste

## Slide 10: Landfills
About 60% of solid waste in the U.S. is sent to landfills
1987: Discovered that landfills on Long Island were contaminating ground water
  Mabro barge left New York with 3,186 tons of garbage in search of a dumping grounds
  Not In My Backyard (NIMBY): we need landfills but no one wants it in their backyard
    Examples of environmental justice

## Slide 11: Sanitary Landfills
Hold waste with little contamination of the surrounding environment as possible
  Federal law prohibits landfills located near geologic faults, wetlands, floodplains or airports.
  Double layered lining constructed with clay or plastic lining at the bottom
  Systems of pipes collects leachate
  When it reaches capacity, covered with a cap of soil and clay
  Leachate regularly collected and tested for toxicity

## Slide 12: Sanitary Landfills
Monitoring the contents: Material least likely to contaminate the environment through leachate or generate methane in put into landfills
  Incentives to recycle aluminum, metals, batteries, motor oil, antifreeze

## Slide 13: Sanitary landfills

## Slide 14: Landfill Costs
Very expensive to construct a landfill
  Tipping fee: trucks weighed before they are tipped into the landfill
    Average 35$ per ton in the US
    Benefits:
      Encourages recycling
      Minimize waste
    Disadvantages:
      May encourage illegal dumping

## Slide 15: Landfills
Disadvantages:
  Located near populations that do not have the resources to object
  Fear of leachate contaminating underground waterways (before and after it is closed)
  Methane can create an explosion hazard
  Due to anaerobic conditions, solid waste doesn’t really decompose

## Slide 16: Incineration
Burning waste materials to reduce their volume and mass
Process:
  MSW is sorted and cleaned
  Heat converts waste into CO2 and H2O released to atmosphere
Ash: particulates that do not combust
  Bottom ash: collected beneath the furnace
  Fly ash: collected beyond the furnace
  Ash is tested for toxicity using weak acid
    Low amount of contaminants landfills, can fill in road construction, used in cement
    High amount of contaminants: special ash landfill
  Waste to energy systems: heat generated by incineration is used rather than released to the atmosphere

## Slide 18: Incineration
Disadvantages:
  Tipping fees are higher ($70 per U.S. ton)
  Incineration releases air pollutants
  Ash more toxic than the original MSW
  Incinerators may not burn all the waste

## Slide 19: Methane Digester:
Methane produced in closed cells can be burned to generate electricity
  Can produce steam to turn a turbine (rotates coils in a magnetic field)

## Slide 20: Homework
Finish Reading Ch. 16
Research
  What is cadmium
  How cadmium can end up as a pollutant in landfills