## Slide 1: SWBAT identify the problems associated with the generation and disposal of hazardous waste. Do Now: What is the difference between superfund sites and brownfields? Who is Lois Gibbs and why is she famous?
APES Unit 10 3/9/16

## Slide 2: Agenda
Lecture
Math!

## Slide 3: Hazardous Waste
Any waste that poses a danger to human health or ecosystems (liquid solid, gas, or sludge)
  Examples: batteries, paints, solvents, pesticides, lawn fertilizers, radioactive waste
  Only 5% is recycled

## Slide 4: Types of hazardous Waste
Corrosive waste: Waste that corrodes (eats away at) metal
Ignitable waste: substances that can easily catch fire (alcohol or gasoline)
Reactive waste: chemically unstable or reacts readily with other compounds, may result in explosions
Toxic waste: creates health risks when inhaled or ingested, or when it comes into contact with skin

## Slide 5: Handling of hazardous waste
Most municipalities don’t have regular collection sites
  Treatment and exposure more expensive than MSW
  Treatment: making hazardous waste more environmentally friendly

## Slide 6: Disposing of hazardous waste
Disposing of hazardous waste: injection wells, surface impoundment, or landfills
  Deep well injection: drilling a hole in the ground that’s below the water table (injected into porous rock)
  Surface impoundment: shallow, lined pools where the hazardous waste evaporates (used for liquid waste)
  Landfills: designated spots for hazardous waste
  Best option: reduce the amount of hazardous waste produced in the first place!

## Slide 7: Radioactive Waste
Yucca Mountain: potential site of disposal for nuclear waste
  Controversial due to NIMBY and the fact that Nevada has no nuclear power plants
Low-level radioactive waste: produce low levels of ionizing radiation
High-level radioactive waste: produce high levels of ionizing radiation

## Slide 8: Legislative Response
U.S. Resource Conservation and Recovery Act (RCRA, 1976):
  Encouraged states to develop comprehensive plans to manage nonhazardous industrial solid waste and MSW
  Sets criteria for municipal solid waste landfills and other solid waste disposal
  Established program for controlling hazardous waste from creation to disposal (cradle to grave)

## Slide 9: Legislative Response
Comprehensive Environmental Response, Compensation and Liability Act (CERCLA or Superfund Act):
  Tax on chemical and petroleum industries
    Revenue from tax funds used to clean up abandoned, non-operating hazardous waste sites
  Authorizes federal government to respond directly to release of chemicals that may pose a threat to human health or the environment
NPL: list of contaminated sites that are eligible for cleanup

## Slide 10: Superfund Sites

## Slide 11: Love Canal
Hazardous Waste landfill where they built a school and housing-development
  Carcinogenic chemicals found in basements
Listed as superfund site and residents evacuated
Lois Gibbs: spokeswoman for the community

## Slide 12: Brownfields
Assisted state and local governments in cleaning up contaminated industrial and commercial land that is not in the superfund category
Examples:
  Dry cleaners, gas, stations, landfills, waterfront

## Slide 13: Brownfield Reclamation

## Slide 14: Life-Cycle Analysis
Examining the materials used and released throughout the lifetime of a product
  Consider energy in producing the product
  Pollution from trucking material to each destination
  Always a cost to waste disposal (direct or indirect)

## Slide 15: Integrated Waste Management
Strategies:
  Source reduction
  Recycling
  Composting
  Landfills and incinerators

## Slide 16: Cradle to Cradle Theory
Minimize waste generation before, after and during manufacturing

## Slide 17: Noise Pollution
Noise pollution: any noise that causes stress or has the potential to damage human health
U.S. Noise Control Act of 1972 gave the EPA power to set emission standards for major sources of noise, including transportation, machinery, and construction.
Occupational Safety and Health Association (OSHA): set limits on the amount of noise that people can be exposed to in the workplace
More noise damage to hearing
  Cells that are involved in hearing do not regenerate loss of hearing is permanent

## Slide 18: Turn and Talk
How is hazardous waste different than MSW?
How can we reduce the production of hazardous waste?

## Slide 19: Math Groups!
Group 1: Rimsha, Monica, Ramlah
Group 2: Cynthia, Wyllana, Amrat
Group 3: Harmanpreet, Uzma, Rahila
Group 4: Shayna, Mahnoor, Hamna, Mehrangiz
Group 5: Desire, Bukurie, Attia, Wendy, Saliha,

## Slide 20: Math Group Rules
Skip to the math portion of the FRQ (c-d)
ALWAYS start with the end
Ask two people before me
Show ALL your work and units

## Slide 21: Homework
Study for the quiz
Start Reading Ch. 17 through page 470 (stop before toxicology)